## Slide 1: Calculating the Lyapunov Exponent
Time Series Analysis of Human Gait Data

## Slide 2: Key Topics
Biological Significance
Algorithm to Lyapunov Exponent
  Reconstruction
  Nearest Neighbor
  Dj(i)
  Curve Fitting
  GUI
Reverse Dynamics
Conclusion

## Slide 3: What is Peripheral Neuropathy?
Peripheral neuropathy is a progressive deterioration of peripheral sensory nerves in the distal extremities.
Affects more than 20 Million Americans.
Symptoms:
  Muscle weakness
  Cramps
  Fasciculation i.e. muscle twitches
  Muscle Loss
  Bone Degeneration

## Slide 4: Causes
A number of factors can cause neuropathies:
Trauma or pressure on the nerve.
Diabetes.
Vitamin deficiencies.
Alcoholism.
Autoimmune diseases.
Other diseases.
Inherited disorders.
Exposure to poisons.

## Slide 5: Why is this being researched?
Studying human gait of affected and non-affected
  Pinpoint the problem areas by comparing both data sets.
  Learning what parts of the body are malfunctioning could help treat peripheral neuropathy.
General contributions
  Accurately measuring stability in human gait could lead to possible prevention of future accidents.

## Slide 6: Data Collection Process
Patients has reflective sensors adhered to anatomical landmarks on the outside of the legs, arms, and head.
Starts walking on treadmill within the range of infrared cameras.
Steady walking on treadmill for approximately 80 seconds.
    Captures 60 angles/second
    Collects 4900 data points.

## Slide 7: Reconstruction
Important to properly capture dynamics of the system
  i.e. position  velocity
Implemented Method of Delays
  Embedding Dimension (n) –variables of the reconstruction (experimentally, dimension of 5 is suggested)
  Lag (L)-number of consecutive vectors to skip for reconstruction

## Slide 8: Reconstruction

## Slide 9: Nearest Neighbor
  dj(i) = ||Xj – Xj’||
Reference point Xj
Nearest neighbor Xj’
  dj(0) = minxj’ ||Xj – Xj’||
  dj(1) = ||Xj + 1– Xj’ + 1||
  ||j – j’|| > mean period

## Slide 10: Dj(i)
Two curve fitting models two Dj(i) algorithms
dj(i)  Cje1(it)
Linear Model
  Previous used fit
  Average the lndj(i) for each i
  lndj(i) lnCj+ 1(it)
Double Exponential Model
  Experimental Model
  Average of dj(i) for each I
  dj(i)  Cje1(it

## Slide 11: Curve Fitting
Linear Model
  lndj(i) lnCj+ 1(it)
  Calculates two linear fits
    short term: 0 – 1 stride
    long term: 4 – 10 stride
Double Exponential Model
  dj(i)  A – Bse-t/s – BLe-t/
  Four unknown variables
    Bs , BL
    s ,L

## Slide 12: Curve Fitting

## Slide 13: Curve Fitting
General model: f(x) = a-bs*exp(-x/ts)-bl*exp(-x/tl)
Coefficients (with 95% confidence bounds): a = 145.9 (145.7, 146) bl = 56.69 (55.93, 57.45) bs = 60.32 (58.33, 62.32) tl = 203.8 (199.8, 207.7) ts = 10.8 (10.15, 11.45)
Goodness of fit: SSE: 4809 R-square: 0.9854 Adjusted R-square: 0.9853 RMSE: 1.794

## Slide 14: GUI Demo

## Slide 15: Reverse Dynamics
We are using an approximation scheme to compute the Lyapunov exponent.
  Using embedding dimension m leads to m Lyapunov exponents
    Spurious exponents
Reverse dynamics can be used to identify spurious exponents.
 |  |  | Book 1 |  | 
 |  |  | Hip | Knee | Ankle
Normal | Short-term |  | 0.0311652 | 0.0345363 | 0.0241968
 | Long-term |  | 0.00133618 | 0.0015417 | 0.00102537
Reverse | Short-term |  | 0.0305798 | 0.0352694 | 0.0276853
 | Long-term |  | 0.00169744 | 0.00172776 | 0.000978649
Results show we have the same exponents under normal and reverse dynamics.

## Slide 16: Conclusion & Acknowledgments
Updates to the graphical user interface (GUI)
  Methods to updating both the single and double exponential, accompanied with a study on
    Reverse Dynamics was established.
Implementing the single and double exponential models in the GUI were not completed this could be added as a further update to the GUI.
We would like to thank Professor Li Li, Professor Lee Hong, Brad Manor, Alvaro Guevara, and Professor Wolenski for all of their helpful comments and advice over the course of the semester.